## Slide 1: Acoustic processing and Pattern recognition of Coins
Written by Chi-Young Jeffrey Lii
With thanks to Ted, and the people in MIRLAB
Overseen by Professor Roger Jang

## Slide 2: Contents
Goals of research
Definition of Important Terms
Program Process
  Research Phase
  Implementation Phase
Demonstration
Question Session

## Slide 3: Stated Goal
Familiarize self with Matlab by using Matlab on a day-to-day-basis
Learn about signal processing, feature extraction, pattern recognition, and classifier training
Applying research done in the MIRLAB, differentiate what kind of coin is being dropped, from the sound alone

## Slide 4: Definition of imporant terms
MATLAB
  State-of-the-Art computing environment and programming language
Signal Processing
Feature Extraction
Pattern Recognition
Classifier Training

## Slide 5: Definition of imporant terms
MATLAB
Signal Processing
  Operations on or Analysis of analog and digital signals
    Example: Detecting the endpoints of a signal
Feature extraction
Pattern Recognition
Classifier Training

## Slide 6: Definition of imporant terms
MATLAB
Signal Processing
Feature Extraction
  Transforming a set of raw data into a set of useful features: A long process
Pattern Recognition
Classifier Training

## Slide 7: Definition of imporant terms
MATLAB
Signal Processing
Feature Extraction
Pattern Recognition
  Study of data patterns and pattern extraction methodology
  Example: Gaussian Mixture Model
Classifier Training

## Slide 9: Research Phase
Record the sound of 4 types of coins dropped 5 times in the same way
Process the files: Extract the Mel-Frequency Cepstral Coefficient
  Unique thirteen number length vector for each .wav file
Vectors are projected on two vectors for easier analysis (Linear Dimension Analysis)

## Slide 10: Research Phase Results
5 sound samples of 1nt, 5nt, 10nt, and 50nt
1nt and 5nt have very unique sounds
10nt and 50nt have similar sounds. Overlap area shown in grey
Best classifier tested to be quadratic (‘qc’)

## Slide 11: Implementation Phase
Low accuracy
  20% accuracy
  Everything tested to be 10nt
  Gaussian mixture model classifier more reliable than Quadratic
  Conclusion: Need more training data – More training data = more accurate

## Slide 12: Imlementation Phase – 220 wav files
Recorded additional 50 wav files for each coin type – Total of 220
  Significantly increased accuracy – close to 95%
  Still some confusion between 10 NT and 50 NT
  Shows overlap between all 4 coin types (Yellow Arrow)